DESCRIPTION

Under this item the contractor shall construct and install filter fabric drop inlet devices as shown on the contract drawings.

MATERIAL

Filter fabric, wood stakes, and/or any other materials necessary meeting the requirements shown on the details.

CONSTRUCTION DETAILS

The filter fabric devices shall be installed as shown on the details prior to construction commencing around the specified drop inlets shown on the plans.  The devices are to be maintained by the contractor throughout the duration of construction.

Once construction activities are complete, the devices shall be removed and disposed as directed by the engineer.

METHOD OF MEASUREMENT

The contractor shall be paid for the number of filter fabric devices actually installed, maintained, removed, and disposed.

BASIS OF PAYMENT

The unit price bid for each filter fabric device shall include the cost of furnishing all necessary labor, materials, and equipment necessary for the installation, maintenance, removal, and disposal to satisfactorily complete the work as determined by the engineer.

Payment will be made under:

| Item No. | Item | Pay Unit |
| --- | --- | --- |
| C209.0102 | Filter Fabric Drop Inlet Protection | EA |