BMP Summary Sheet

Department Name:

Category of Municipal Operations:   Municipal Building Maintenance

BMP Title: Outdoor Container Storage

BMP Description: Protect materials from rainfall, runon, runoff, and wind dispersal by covering the storage area with a roof. Use covered dumpsters for waste containers. Use a ‘doghouse’ structure for storage of liquid containers. Berm or surround tank or container with secondary containment system. Provide barriers around tanks such as posts to prevent collision damage from vehicles. Place tight fitting lids on all containers. Raise containers off the ground with provisions for spill control and secondary containment. Contain the material in such a way that if a leak or spill occurs, the contents will not drain to the storm drain or other waters. Place containers in a lean-to structure or otherwise covered to keep rainfall away.

Measurable Goals: Implementation of a recycling program.

Timeline/Implementation Schedule:

Specific Components and Notes:

Responsible Party for this BMP Indicate who specifically is responsible for the implementation and monitoring of this BMP. This should be the individual who is actively involved with the BMP. Name: Department: Phone: E-mail:

BMP Summary Sheet

Department Name:

Category of Municipal Operations: Municipal Building Maintenance

BMP Title: Outdoor Loading and Unloading

BMP Description: Develop an operations plan that describes procedures for loading and unloading. Do not conduct loading and unloading during wet weather if possible. Cover designated loading areas to reduce exposure of materials to rain. Design loading areas to prevent stormwater runon which would include grading or berming the area, and positioning roof downspouts so they direct stormwater away from the loading area. Load all materials and equipment in covered areas such as building overhangs at loading docks. Pave loading areas with concrete instead of asphalt. Avoid placing storm drains in the area.

Measurable Goals:

Timeline/Implementation Schedule:

Specific Components and Notes:

Responsible Party for this BMP Indicate who specifically is responsible for the implementation and monitoring of this BMP. This should be the individual who is actively involved with the BMP. Name: Department: Phone: E-mail:

BMP Summary Sheet

Department Name:

Category of Municipal Operations:     Municipal Building Maintenance

BMP Title: Plaza and Sidewalk Cleaning

BMP Description: Use dry cleaning methods whenever practical for surface cleaning activities. Use the least toxic materials available (e.g. water based paints, gels or sprays for graffiti removal) Regularly broom (dry) sweep sidewalks plaza and parking lot areas to minimize cleaning with water Sweep, collect, and dispose of debris and trash before washing Block the storm drain or contain runoff when cleaning with water. Discharge wash water to landscaping or collect water and pump to a tank or discharge to the sanitary sewer. Block storm drain inlets or contain runoff when washing parking areas, driveways or drive-throughs. Use absorbents to pick up oil; then sweep dry. Clean with or without soap. Collect water and pump to a tank or discharge to the sanitary sewer.

Measurable Goals: Report number of alternative products or methods used.

Timeline/Implementation Schedule:

Specific Components and Notes:

Responsible Party for this BMP Indicate who specifically is responsible for the implementation and monitoring of this BMP. This should be the individual who is actively involved with the BMP. Name: Department: Phone: E-mail:

BMP Summary Sheet

Department Name:

Minimum Control Measure: Municipal Building Maintenance (Also 						applicable to most operations and facilities)

BMP Title: Spill Prevention, Control, & Cleanup

BMP Description: Move material handling indoors, under cover, or away from storm drains or sensitive water bodies, if possible. Properly label all containers so contents are easily identifiable. Berm storage areas so that if a spill of leak occurs, the material is contained. Cover outside storage areas either with a permanent structure or a seasonal one so that rain cannot contact materials. Check containers often for leaks or spills, and replace deteriorating containers with ones in good condition. Store, contain, and transfer liquid materials in such a manner that if the contents spilled, they would not discharge or be washed into the storm drain, surface waters, or groundwater. Place drip pans or absorbent materials beneath all mounted taps and all potential drip and spill locations during the filling and unloading of containers. For field programs, only transport the minimum amount of material needed for the daily activities and transfer materials between containers at a municipal yard where leaks and spills are easier to control. If paved, sweep and clean storage areas monthly. Do not hose down area unless water is being collected and disposed properly. Install a spill control device in any catch basins that collect runoff from areas storing materials that separate and float on water. Protect catch basins while a conducting field activity so if a spill does occur, the material is contained.

Measurable Goals:

Timeline/Implementation Schedule:

Specific Components and Notes:

Responsible Party for this BMP Indicate who specifically is responsible for the implementation and monitoring of this BMP. This should be the individual who is actively involved with the BMP. Name: Department: Phone: E-mail: