BMP Summary Sheet

Department Name:

Category of Municipal Operations:    Stormwater System Maintenance

BMP Title: Catch Basin/ Inlet Structures

BMP Description: Staff should regularly inspect the storm drain system to identify problems. Any deterioration threatening structural integrity should be immediately repaired. Catch basins should be cleaned before the sump is 40% full. Cleaning frequently should be scheduled as needed to meet this standard. Clean catch basins, inlets and other conveyance structures in high pollution load areas before the wet season to remove accumulated sediment and debris. Conduct inspections more frequently during wet season for problem areas where sediment or trash accumulates more often. Keep accurate logs of the number of catch basins cleaned and record the amount of waste collected. Store any collected waste appropriately away from inlets or streams. If waste is collected by vactor follow procedures for dumping of vactor waste.

Measurable Goals: Approximate quantity (tons or cubic yards) of material cleaned from structures Frequency of scheduled cleaning

Timeline/Implementation Schedule:

Specific Components and Notes:

Responsible Party for this BMP Indicate who specifically is responsible for the implementation and monitoring of this BMP. This should be the individual who is actively involved with the BMP. Name: Department: Phone: E-mail:

BMP Summary Sheet

Department Name:

Category of Municipal Operations:    Stormwater System Maintenance

BMP Title: Open Channel, Ditch Maintenance

BMP Description: Consider modification of storm channel characteristics to improve channel hydraulics, to increase pollutant removals, and to enhance channel/creek aesthetic and habitat value. If ditch scraping is necessary do it in patches with vegetated strips left down slope to capture sediments. Use hydroseeding immediately after scraping. Hydroseed early in the season to allow sufficient growing time Do not hydroseed immediately before a rain

Measurable Goals: Approximate length of open drainage ditches maintained with enhanced implementation of erosion control practices in ditch (e.g. hydroseeding)

Timeline/Implementation Schedule:

Specific Components and Notes:

Responsible Party for this BMP Indicate who specifically is responsible for the implementation and monitoring of this BMP. This should be the individual who is actively involved with the BMP. Name: Department: Phone: E-mail:

BMP Summary Sheet

Department Name:

Category of Municipal Operations:    Stormwater System Maintenance

BMP Title: Storm Sewer Conveyance System

BMP Description: Locate reaches of storm sewers with deposit problems and develop a flushing schedule that keeps the pipe clear of excessive buildup. Collect flushed effluent by vactor or pump to the sanitary sewer During routine maintenance field staff should look for evidence of illegal discharges or illicit connections. Any signs of spills, dumping or illicit connections should be followed up according to the illicit discharge program.

Measurable Goals: Length of storm drain pipe cleaned or repaired Number of outfalls cleaned Upgrades or technology improvements implemented in overall system Staff training or continuing education activities

Timeline/Implementation Schedule:

Specific Components and Notes:

Responsible Party for this BMP Indicate who specifically is responsible for the implementation and monitoring of this BMP. This should be the individual who is actively involved with the BMP. Name: Department: Phone: E-mail: